## Slide 1
Scale-up of a photocatalytic reactor for the degradation of pesticides at source Indira Menezes, Carlos J. Pestana, Bruce Petrie and Linda A. Lawton Robert Gordon University, Sir Ian Wood Building, Garthdee Road AB10 7GJ, United Kingdom Email: i.de-menezes-castro@rgu.ac.uk www.hydronationscholars.scot
Introduction
Pesticides find their way into natural environments due to rainfall runoff, agricultural activities and incomplete removal by conventional treatments.
Photocatalysis can be applied for the removal of pesticides – a catalyst needs to be illuminated by light of sufficiently high energy which will ultimately produce radicals with high oxidative power.
Graphitic carbon nitride (g-C3N4) coated beads and UV-A light emitting diodes (LEDs) photocatalysis can be used as an economical alternative technology for pesticide removal.
It is necessary to develop an economical and safe alternative that can be applied at source to remove pesticides prior to the treatment plant or before discharge into the environment.
Pesticides in the environment
1
Catalyst and
light source
selection
Photocatalytic system optimisation
Bench-scale pesticide degradation
Reactor scale-up
2
3
4
Future work
Design, test and optimise prototype reactor incorporating UV-A LEDs and g-C3N4 coated beads
Deploy and evaluate photocatalytic reactors in selected farms across Scotland
Potential application in Scottish salmon farms
Non-waterproof
UV-A LED
Reactor
prototype
Waterproof
LED tubing
TiO2 and g-C3N4 coated beads
Beads made with recycled glass were coated with different catalyst. TiO2 and g-C3N4 coated beads and different light sources (UV-A and visible light) were evaluated for best photocatalytic performance.
Optimal initial solution pH and catalyst load were determined to better understand the optimal conditions for the photocatalytic system.
The herbicide diuron was used as a model compound.
Photocatalytic degradation of diuron by UV-A LEDs and and g-C3N4 coated beads
Two-part resin
5
Treatment unit implementation
UV-A LEDs and g-C3N4 coated beads were successful on the removal of pesticides. All pesticides tested were completely removed within 48 hours. Degradation products might have contributed to acetamiprid concentration.