## Slide 1: Safeguarding and improving raw water quality by increasing catchment resilience
Scottish Water Catchment Conference, 06/09/2018
Carolin Vorstius1, John Rowan1, Iain Brown1,
Zoe Frogbrook2, Javier Palarea-Albaladejo3
1School of Social Sciences, University of Dundee, 2Scottish Water,
3Biomatehematics and Statistics Scotland

## Slide 2: Context
Drinking water: An essential commodity
Multiple and mounting pressures on our water resources
Climate and land use changes:
Insecurity of stable supply of high quality drinking water
Rising treatment costs
Need to target mitigation measures
Strategic long-term investments into treatment

## Slide 3: Key questions
What do the catchments that we use as drinking water resources in Scotland look like and what conditions and pressures act on their water quality?
How are catchments likely to change in future and what does this mean for the water quality they yield?
Where can catchment-based mitigation measures help to improve and safeguard water quality?
What are the economical an societal advantages of implementing such measures?

## Slide 4: How? - Project steps
1) What do the catchments that we use as drinking water resources in Scotland look like and what conditions and pressures act on their water quality?

## Slide 5: How? - Project steps
2) How are catchments likely to change in future and what does this mean for the water quality they yield?

## Slide 6: How? - Project steps
3) Where can catchment-based mitigation measures help to improve and safeguard water quality?

## Slide 7: How? - Project steps
Ecosystem Services Assessment
4) What are the economical an societal advantages of implementing such measures?

## Slide 8: Projected outcomes
Risk assessment:
  Identification of catchments at risk of deteriorating water quality
  Identification of contributing factors
  Estimate of possible/probable effects of mitigation measures
Ecosystem Services Assessment:
  Identification of benefits and trade-offs of managing for water quality

## Slide 9: Catchment characterisation
398 active catchments (141 rivers, 49 lochs, 146 impounding reservoirs, 21 springs, 41 boreholes)
Histogram of catchment area in km2
Distribution of slopes

## Slide 10: Catchment characterisation

## Slide 11: Catchment characterisation

## Slide 12
Aluminium
Colour
Iron
Turbidity
pH
E. coli
Water quality
Catchment medians
Notes: Very high outliers

## Slide 13
Water quality
Catchment medians
 | Minimum | 5th | 25th | Median | Mean | 75th | 95th | Maximum | Consumer’s tab
Aluminium (µg Al/l) | 9 | 24.65 | 42.25 | 64.75 | 76.26 | 92.88 | 168.45 | 404 | 200
Colour (mg/l Pt/Co) | 2 | 11 | 24 | 33.75 | 38.95 | 49.62 | 81 | 167.5 | 20
Iron (µg Fe/l) | 7 | 44.95 | 108.1 | 179.5 | 267.4 | 361.8 | 783.4 | 1465 | 200
Manganese (µg Mn/l) | 1 | 2 | 5.5 | 13 | 22.12 | 27 | 60.39 | 405.5 | 50
pH | 5.5 | 6.2 | 6.7 | 7.1 | 7.06 | 7.4 | 7.7 | 8.4 | 6.5-9.5
Turbidity (NTU) | 0.2 | 0.3 | 0.45 | 0.6 | 1.03 | 1 | 4 | 6.1 | 4†
Coliforms (CFU in 100ml) | 9 | 28.65 | 88 | 190 | 279.2 | 285 | 552 | 4950 | 0
E. coli (CFU in 100ml) | 0 | 0 | 1 | 4.25 | 17.62 | 10 | 40.17 | 580 | 0
Notes: Very high outliers

## Slide 14: Water quality Time series

## Slide 15: Typology and models Data analysis issues
Key issues in the data analysis:
  Different sample sizes
  Very skewed distributions within catchments as well as catchment medians
  Data for some catchments show seasonal patterns
  Very high outliers
  Of interest are middle points of the data as well as extremes
Analysis performed:
  Principal Component Analysis
  Cluster Analysis
  Multi-target regression trees

## Slide 16: Typology and models PCA

## Slide 17: Data analysis Cluster Analysis
Notes: Silhouette width 0.21

## Slide 18: Data analysis Regression trees
Colour – medians and 95th percentiles
SlopeSteep > 20.18
+--yes: SlopeSteep > 36.5
| +--yes: [16.23, 37.12]: 13
| +--no: [29.11, 57.51]: 22
+--no: Peat > 81.69
+--yes: [58.8, 130.65]: 28
+--no: [37.75, 74.47]: 45
RMSE: [24.3, 48.12]
R2: [0.48, 0.42]
E. coli– medians and 95th percentiles
PrecdaysAnnual > 1.77
+--yes: Arable15 > 0.05
| +--yes: SlopeLittle > 18.57
| | +--yes: [16.12, 169.54]: 8
| | +--no: [77.25, 1700.5]: 2
| +--no: Imprgrass15 > 28.01
| +--yes: [15, 418.25]: 2
| +--no: ReliefRatio > 0.129
| +--yes: Source = 'Loch'
| | +--yes: [10, 586.32]: 2
| | +--no: [7.83, 111.14]: 21
| +--no: [5.50, 72.67]: 69
+--no: [292.5, 2064.37]: 4
RMSE: [55.46, 660.57]
R2: [-0.03, -0.04]

## Slide 19: Typology and models Further approach
Lead areas identified from data analysis:
  DOC release from peatland – contributing conditions and climate change
  Expansion of areas suitable for (more intensive) agriculture through climate change
Next steps:
  Analyse a subset of catchment with high peatland cover with regard to catchment conditions and colour concentrations
  Analyse a subset of catchments with regard to relationships between certain types of land use (arable agriculture and improved grassland) and E. coli contamination

## Slide 20: Safeguarding and improving raw water quality by increasing catchment resilience
Thank you!
a.c.vorstius@dundee.ac.uk
And thank you to…
Scottish Water for providing the data
The Scottish Government (Hydro Nation Scholars Programme) for funding this research

## Slide 21: Data analysis PCA
 | PC1 | PC2 | PC3
Water quality | Loadings† |  | 
Aluminium Median | 0.39* | -0.09 | -0.12
Colour Median | 0.39* | -0.33* | -0.09
Iron Median | 0.48* | -0.08 | -0.02
Manganese Median | 0.42* | -0.09 | 0.33*
pH Median | -0.09* | 0.46* | 0.66*
Turbidity Median | 0.43* | 0.08 | 0.33*
Coliform Median | 0.18* | 0.50* | -0.57*
E.coli Median | 0.24* | 0.63* | -0.09
Catchment characteristics | Correlations ‡ |  | 
Deciduous woodland |  | 0.16 | 
Arable |  | 0.42 | 
Improved grassland |  | 0.29 | 
Urban | 0.25 | 0.39 | 
Relief ratio | -0.31 |  | 
Little slope | 0.26 |  | 
Steep slope | -0.23 |  | 
Sandstone |  |  | 0.20
Mean monthly total rainfall | -0.19 |  | -0.22
Mean number of days per months with >10mm precipitation | -0.17 |  | -0.21
Variability explained:
PC1: 46%
PC2: 20%
PC3: 14%
Total: 80%

## Slide 22: Data analysis Cluster Analysis

## Slide 23: Data analysis Cluster Analysis

## Slide 24: Data analysis Cluster Analysis